## Slide 1
Shim coils – RF coils

## Slide 2: Shim coils

## Slide 3: Magnetic field inhomogeneities
It is impossible to create an electromagnet which produces a perfectly homogenous magnetic field.
?
Design limitations

## Slide 4: Magnetic field inhomogeneities
The strength of the field is dependent on the distance between the loops.
Unevenly spaced loops create inhomogeneities in the main magnetic field.
These inhomogeneities are measured in parts per million (ppm).

## Slide 5: Field homogeneity
Required homogeneity for:
- Imaging purposes: 10 ppm
- Spectroscopic procedures (MRS): a more homogeneous environment of 1ppm.

## Slide 6: Shimming and shim coil
Inhomogeneities in the external field are undesirable and can cause artifacts.
To correct for these inhomogeneities, another loop of current-carrying wire is placed in the area of the inhomogeneity.
This compensates for the inhomogeneities in the main magnetic field  Creates magnetic field homogeneity or evenness.
This process is called shimming.
Extra loop of wire is called a shim coil.

## Slide 7: Shim coils
These coils are used to create a more uniform external magnetic field B0.
Shim coils help to minimize (although not totally eliminate) such variations.

## Slide 8: Shimming
Active shimming:
Magnet shimming with loops of current carrying wire
Passive shimming:
Magnet shimming with metal

## Slide 9: Shimming
The shim system requires a power supply which is separate from other power supplies within the system.

## Slide 10: RF coils

## Slide 11: RF coils
RF coils are one of the most important components that affect image quality.
A transmitter coil sends or transmits an RF pulse.
A receiver coil receives an RF pulse.
Some coils such as body coils and head coils are both transmitters and receivers (T/R).
Others are just receivers (e.g., surface coils).

## Slide 12: Body coil
The body coil is a fixed part of the magnet that surrounds the patient and is used in a variety of applications as a transmitter and/or receiver.

## Slide 13: Head coil
A head coil surrounds the patient's head and may act as both a transmitter and receiver or just as a receiver.

## Slide 14: RF transmitter coil
It is a loop of wire
Passing current through RF transmitter coil 
Oscillating secondary magnetic field (B1) 
Creating RF pulse

## Slide 15: RF transmitter coils
The secondary magnetic field (B1) must be situated at the right angles to the main magnetic field (B0)

## Slide 16: Receiver coils
If a loop of wire is exposed to an oscillating field, a current is induced in the loop. This current and the resulting voltage constitute the MR signal.

## Slide 17: MRI instrumentations

## Slide 18: References
Westbrook C, MRI at a Glance, Blackwell Science, Second edition
Hashemi, RH and Brandy WG. MRI the Basics, Wolters Kluwer, Second edition
Blink EJ, mri : Physics, 2004
Westbrook C, Handbook of MRI technique, Blackwell Science, Second edition