## Slide 1
RF coils (2)

## Slide 2: RF coils
Configuration of RF transmitter and receiver coils directly affect the MRI signal.

## Slide 3: Coil types
The choice of coil for any examination is one of the most important factors that determine the SNR of the image.
Most common currently available coils:
Volume coils
Surface/local coils
Phased array coils

## Slide 4: Volume coils

## Slide 5: Volume coils
Most of them are quadrature coils.
Quadrature coils use 2 pairs of coils to transmit RF pulse and receive signal  improving SNR

## Slide 6: Volume coils
Head coil
Knee coil

## Slide 7: Volume coils
Advantages:
- Encompassing large arias of anatomy
- Yielding a uniform signal across whole FOV
Notes: Encompassingدربرگیرنده, شامل:

## Slide 8: Surface coils

## Slide 9: Surface coils
Surface coils are placed close to the area under examination such as:
The temporo-mandibular joint
The orbits
The shoulder
The coil consists of a single or double loop of copper wire.

## Slide 10: Surface coils

## Slide 11: Surface coils
To improve SNR for structures near the skin surface
Designed to fit a certain area
Increase SNR compared to volume coils
?
Close to the region of interest (ROI)
Notes: Only receiver
Transmitter coil?
Usually body coil

## Slide 12: Surface coils
Only receiver
Using body coil as transmitter
In case of a circular surface coil, signal is received up to the edges of the coil and to a depth equal to the radius of the coil.

## Slide 13: Surface coils disadvantage
The disadvantage is that they loose signal uniformity very quickly when you move away from the coil.

## Slide 14: Surface coils
Advantages of using two surface coil linked together:
- Increases SNR
- Increases uniformity of signal
Helmholtz

## Slide 15: Phased array coils

## Slide 16: Phased array coils
These coils contain multiple small surface coils.
These coils allow faster scanning with finer details.

## Slide 17: Phased array coils advantages
The signal from each coil is combined with the signals of other coils to form one image.
This image has both advantages of small coil and large coil:
Improved SNR
Increased coverage

## Slide 18: Phased array coils
Applications:
To examine large areas such as entire length of the spinal cord
To improve signal uniformity and intensity in small areas such as breast

## Slide 19: Phased array coils
Examples:
Spine coil
Breast coil
Pelvic coil
Spine array coil

## Slide 20: References
Westbrook C, MRI at a Glance, Blackwell Science, Second edition
Hashemi, RH and Brandy WG. MRI the Basics, Wolters Kluwer, Second edition
Blink EJ, mri : Physics, 2004
Westbrook C, Handbook of MRI technique, Blackwell Science, Second edition